## Slide 1: Advanced Computer Graphics
CSE 163 [Spring 2017], Lecture 14
Ravi Ramamoorthi
http://www.cs.ucsd.edu/~ravir

## Slide 2: To Do
Assignment 2 due May 19
  Any last minute issues or questions?
Next two lectures: Imaging, Texture Synthesis
  Then resume rendering, animation

## Slide 3: Computational Imaging
Digital cameras now commonplace
Can we use computation for better images
  Many novel capabilities relative to film
And new ways of processing images
Is this computer graphics, optics, or image proc?
  All of the above; many rendering ideas apply
  Application shift. Computer aided design to movies/games to photography (big market)
Brief lecture. Subject of whole conference ICCP
  Industry: Light Field cameras, Google glass, …

## Slide 4: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 5: How do we see the world?
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide by Steve Seitz

## Slide 6: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Slide by Steve Seitz
Notes: It gets inverted

## Slide 7: Pinhole camera model
Pinhole model:
  Captures pencil of rays – all rays through a single point
  The point is called Center of Projection (COP)
  The image is formed on the Image Plane
  Effective focal length f is distance from COP to Image Plane
Slide by Steve Seitz

## Slide 8: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)

## Slide 9: Funny things happen…

## Slide 10: Parallel lines aren’t…
Figure by David Forsyth

## Slide 11: Lengths can’t be trusted...
Figure by David Forsyth
B’
C’
A’

## Slide 12: …but humans adapt!
http://www.michaelbach.de/ot/sze_muelue/index.html
Müller-Lyer Illusion
We don’t make measurements in the image plane

## Slide 13: Camera Obscura
The first camera
  Known to Aristotle
  Depth of the room is the effective focal length
Camera Obscura, Gemma Frisius, 1558

## Slide 14: From Pinhole to Lenses
Computer graphics assumes pinhole model
But making aperture narrow limits light
Making aperture large causes blurriness
Real cameras have lenses to collect more light, and focus it on the image plane
(Kolb et al. 95 simulates lens effects rendering)

## Slide 15: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?

## Slide 16: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Less light gets through
Slide by Steve Seitz

## Slide 17: The reason for lenses
Slide by Steve Seitz

## Slide 18: Focus and Defocus
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape/separation of lens changes this distance
“circle of
confusion”
Slide by Steve Seitz

## Slide 19: Thin lenses
Thin lens equation:
  Any object point satisfying this equation is in focus
  What is the shape of the focus region?
  How can we change the focus region?
  Thin lens applet: http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html (by Fu-Kwun Hwang )
Slide by Steve Seitz

## Slide 20: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm

## Slide 21: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 22
Light Field Inside a Camera
Notes: 22

## Slide 23: Lenslet-based Light Field camera
[Adelson and Wang, 1992, Ng et al. 2005 ]
Light Field Inside a Camera
Notes: 23

## Slide 24: Stanford Plenoptic Camera [Ng et al 2005]
4000 × 4000 pixels ÷ 292 × 292 lenses = 14 × 14 pixels per lens
Contax medium format camera
Kodak 16-megapixel sensor
Adaptive Optics microlens array
125μ square-sided microlenses
Notes: 24

## Slide 25: Digital Refocusing
[Ng et al 2005]
Demo at: https://pictures.lytro.com/
Notes: 25

## Slide 26
Mask based Light Field Camera
Mask
Sensor
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 26

## Slide 27
1/f0
Mask Tile
Cosine Mask Used

## Slide 28
Captured 2D Photo
Encoding due to Mask
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 28

## Slide 29
2D FFT
Traditional Camera Photo
Heterodyne Camera Photo
Magnitude of 2D FFT
2D FFT
Magnitude of 2D FFT
Notes: 29

## Slide 30: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 31
Out of Focus Photo: Coded Aperture
Engineering the PSF when you cannot capture Lightfield
Notes: 31

## Slide 32
In Focus Photo
LED
2D Photo
Notes: 32

## Slide 33
Out of Focus Photo: Open Aperture
Notes: 33

## Slide 34
Out of Focus Photo: Coded Aperture
Notes: 34

## Slide 35: Captured Blurred Photo
[Veeraraghavan, Raskar, Agrawal, Tumblin, Mohan, Siggraph 2007 ]
Notes: 35
Reversibly encode all the information in this otherwise blurred photo

## Slide 36
Refocused on Person
Increase DoF + large aperture
Notes: 36
The glint out of focus shows the unusual pattern.

## Slide 37: Outline
Image formation, basic lens-based camera
Light Field camera
Coded aperture depth of field
Flutter shutter (coded aperture shutter)
Many many more old, new innovations

## Slide 38
Traditional Camera
Shutter is OPEN
Notes: How blurring happens in traditional camera

## Slide 39
Our Camera
Flutter Shutter
Notes: And in flutter shutter camera

## Slide 40
Shutter is OPEN and CLOSED

## Slide 41
Lab Setup

## Slide 42
Blurring
==
Convolution
Traditional Camera: Box Filter
Sync Function
Notes: How is the blurred image formed? It’s a convolution with box filter

## Slide 43
Flutter Shutter: Coded Filter
Preserves High Frequencies!!!
Notes: Coded exposure makes the filter broadband

## Slide 44
Comparison

## Slide 45
Inverse Filter Unstable
Inverse Filter stable

## Slide 46
Notes: Deblurring using the single photo. Blur is 60 pixels

## Slide 47
Input Image

## Slide 48
Rectified Crop
Deblurred Result
Notes: Result: Blur is 235 pixels, all text can be read