## Slide 1: Computer Graphics
CSE 167 [Win 23], Lecture 5: Viewing
Ravi Ramamoorthi
http://viscomp.ucsd.edu/classes/cse167/wi23

## Slide 2: To Do
Questions/concerns about assignment 1?
Remember it is due Friday! (Jan 27).
Ask me or TAs re problems

## Slide 3: Motivation
We have seen transforms (between coord systems)
But all that is in 3D
We still need to make a 2D picture
Project 3D to 2D. How do we do this?
This lecture is about viewing transformations

## Slide 4: Summary: The Whole Viewing Pipeline
Model
transformation
Camera
Transformation
(gluLookAt)
Perspective
Transformation
(gluPerspective)
Viewport
transformation
Raster
transformation
Model coordinates
World coordinates
Eye coordinates
Screen coordinates
Window coordinates
Device coordinates
Slide courtesy Greg Humphreys

## Slide 5: Demo (Projection Tutorial)
Nate Robbins OpenGL tutors
Projection tutorial
Download others

## Slide 6: What we’ve seen so far
Transforms (translation, rotation, scale) as 4x4 homogeneous matrices
Last row always 0 0 0 1. Last w component always 1
For viewing (perspective), we will use that last row and w component no longer 1 (must divide by it)

## Slide 7: Outline
Orthographic projection (simpler)
Perspective projection, basic idea
Derivation of gluPerspective (handout: glFrustum)
Brief discussion of nonlinear mapping in z

## Slide 8: Projections
To lower dimensional space (here 3D -> 2D)
Preserve straight lines
Trivial example: Drop one coordinate (Orthographic)

## Slide 9: Orthographic Projection
Characteristic: Parallel lines remain parallel
Useful for technical drawings etc.
Orthographic
Perspective

## Slide 10: Example
Simply project onto xy plane, drop z coordinate

## Slide 11: In general
We have a cuboid that we want to map to the normalized or square cube from [-1, +1] in all axes
We have parameters of cuboid (l,r ; t,b; n,f)
x
z
y
l
r
t
b
n
f
x
z
Translate
y
x
z
y
Scale

## Slide 12: Orthographic Matrix
First center cuboid by translating
Then scale into unit cube
x
z
y
l
r
t
b
n
f
x
z
Translate
y
x
z
y
Scale

## Slide 13: Transformation Matrix
Scale
Translation (centering)

## Slide 14: Caveats
Looking down –z, f and n are negative (n > f)
OpenGL convention: positive n, f, negate internally
x
z
y
l
r
t
b
n
f
x
z
Translate
y
x
z
y
Scale

## Slide 15: Final Result

## Slide 16: Outline
Orthographic projection (simpler)
Perspective projection, basic idea
Derivation of gluPerspective (handout: glFrustum)
Brief discussion of nonlinear mapping in z

## Slide 17: Perspective Projection
Most common computer graphics, art, visual system
Further objects are smaller (size, inverse distance)
Parallel lines not parallel; converge to single point
B
A’
B’
Center of projection
(camera/eye location)
A
Plane of Projection
Slides inspired by Greg Humphreys

## Slide 18: Funny things happen…

## Slide 19: Perspective Video 1
https://www.youtube.com/watch?v=F5WA26W4JaM&list=PLWfDJ5nla8UpwShx-lzLJqcp575fKpsSO&index=11
Steve Seitz UW 5 minute videos
more detail regarding lenses and actual cameras than needed for course (good to know)

## Slide 20: Overhead View of Our Screen
Looks like we’ve got some nice similar triangles here?

## Slide 21: In Matrices
Note negation of z coord (focal plane –d)
(Only) last row affected (no longer 0 0 0 1)
w coord will no longer = 1. Must divide at end

## Slide 22: Verify

## Slide 23: Perspective Video 2
https://www.youtube.com/watch?v=g7Pb8mrwcJ0&list=PLWfDJ5nla8UpwShx-lzLJqcp575fKpsSO&index=12
Steve Seitz UW 5 minute videos
more detail regarding lenses and actual cameras than needed for course (good to know)

## Slide 24: Outline
Orthographic projection (simpler)
Perspective projection, basic idea
Derivation of gluPerspective (handout: glFrustum)
Brief discussion of nonlinear mapping in z

## Slide 25: Remember projection tutorial

## Slide 26: Viewing Frustum
Near plane
Far plane

## Slide 27: Screen (Projection Plane)
Field of view
(fovy)
width
height
Aspect ratio = width / height

## Slide 28: gluPerspective
gluPerspective(fovy, aspect, zNear > 0, zFar > 0)
Fovy, aspect control fov in x, y directions
zNear, zFar control viewing frustum

## Slide 29: Overhead View of Our Screen

## Slide 30: In Matrices
Simplest form:
Aspect ratio taken into account
Homogeneous, simpler to multiply through by d
Must map z vals based on near, far planes (not yet)

## Slide 31: In Matrices
A and B selected to map n and f to -1, +1 respectively

## Slide 32: Z mapping derivation
Simultaneous equations?

## Slide 33: Outline
Orthographic projection (simpler)
Perspective projection, basic idea
Derivation of gluPerspective (handout: glFrustum)
Brief discussion of nonlinear mapping in z

## Slide 34: Mapping of Z is nonlinear
Many mappings proposed: all have nonlinearities
Advantage: handles range of depths (10cm – 100m)
Disadvantage: depth resolution not uniform
More close to near plane, less further away
Common mistake: set near = 0, far = infty. Don’t do this. Can’t set near = 0; lose depth resolution.
We discuss this more in review session

## Slide 35: Summary: The Whole Viewing Pipeline
Model
transformation
Camera
Transformation
(gluLookAt)
Perspective
Transformation
(gluPerspective)
Viewport
transformation
Raster
transformation
Model coordinates
World coordinates
Eye coordinates
Screen coordinates
Window coordinates
Device coordinates
Slide courtesy Greg Humphreys