## Slide 1: Computer Graphics II: Rendering
CSE 168[Spr 20],Lecture 10: Materials and BRDFs Ravi Ramamoorthi
http://viscomp.ucsd.edu/classes/cse168/sp20

## Slide 2: To Do
Start working on homework 3. Ask me if problems
Also homework 4. Have covered material
Start thinking about final project
Some slides courtesy Steve Rotenberg and Pat Hanrahan

## Slide 3: Materials and BRDFs
Key part of renderer: different materials/BRDFs
Abstract BRDF/Material interface (for MIS)
  Evaluate (for given incident, outgoing direction)
  Sample (given outgoing, importance sample incident)
  PDF (for MIS, evaluate sampling PDF arbitrary direction)
  Also for value of sample, need to compute eval/PDF (sometimes can simplify this, new value function=eval/PDF)
Any physical or non-physical BRDF must fit above
  Evaluation is usually easy (BRDF formula)
  Can encompass analytic formulae, table measurements
  Sampling can be hard and is crucial (see my 2004 paper for general importance sampling, special cases for some)
  PDF function can be non-trivial, make sure math correct

## Slide 4: Diffuse Surfaces
Simplest Case: Lambertian Reflectance
BRDF is simply a constant:
Note energy conservation, divide albedo by π
Note cosine incident term in final evaluation
Evaluate BRDF is straightforward
Sample? Sample hemisphere (or cosine-weight)
PDF is or (if cosine-weight)
Value/weight with cosine sampling is simply

## Slide 5: Oren-Nayar Model
Generalization of Lambert’s Reflectance Model (SIGGRAPH 94, rough diffuse [shadows, interreflections])
From Wikipedia
Importance sampling can be complicated
(but exact sampling is not required)
Simplest: Lambertian sampling/PDF
But Eval uses Oren-Nayar; Eval/PDF
(will cancel leading Lambertian term only)

## Slide 6: Fresnel Surfaces
Idealized Fresnel surfaces are perfectly smooth boundary between dielectric (air,glass,water) and another dielectric, or a dielectric and a metal
Beam splits into reflected/refracted (Snell’s law)

## Slide 7: Optical Manhole

## Slide 8: Fresnel Surfaces
Idealized Fresnel surfaces are perfectly smooth boundary between dielectric (air,glass,water) and another dielectric, or a dielectric and a metal
Beam splits into reflected/refracted (Snell’s law)

## Slide 9: Experiment

## Slide 10: Fresnel Reflectance

## Slide 11: Fresnel Reflectance

## Slide 12: Reflection from Metals

## Slide 13: Cook-Torrance Reflection

## Slide 14: Cook-Torrance Reflection

## Slide 15: (Cook-)Torrance-Sparrow
Assume the surface is made up grooves at the microscopic level. (General Microfacet Theory)
Assume the faces of these grooves (called microfacets) are perfect reflectors.
Take into account 3 phenomena
Shadowing
Masking
Interreflection

## Slide 16: (Cook-)Torrance-Sparrow
Fresnel term:
allows for wavelength dependency
Geometric Attenuation:
reduces the output based on the amount of shadowing or masking that occurs.
Distribution:
distribution function determines what percentage of microfacets are oriented to reflect in the viewer direction.
How much of the macroscopic surface is visible to the light source
How much of the macroscopic surface is visible to the viewer

## Slide 25: Microfacet BRDFs (“Little Faces”)

## Slide 26: Reflection of the Sun from Waves

## Slide 27: Microfacet Distributions

## Slide 28: Beckmann Distribution

## Slide 29: Beckmann Distribution

## Slide 30: Trowbridge-Reitz (GGX) Distribution

## Slide 31: Trowbridge-Reitz (GGX) Distribution

## Slide 37: BRDF Sampling
Have dealt with BRDF evaluation, need importance sampling and PDF functions for MIS
In 2004, no good importance sampling schemes for most BRDFs, including common Torrance-Sparrow
From Lawrence et al. 04, factor BRDF into data-driven terms that can each be importance sampled
Now some form of light/BRDF sampling common in production (standard in RenderMan 16, 2011-)

## Slide 38: Motivation
Cook-Torrance
Measured Metallic-Blue
Measured Plastic
Measured Nickel
Notes: So far, however, the state of the art has made it difficult to use these complex BRDFs in standard global illumination algorithms. For example, we would like to render a scene with several different measured and complex-analytic BRDFs using Monte Carlo path tracing, but there are no good techniques for importance sampling these BRDFs.
so far state of the art has made it difficult to use these complex BRDFs in global illumination algorithms where the norm is still
using simple BRDFs like the Phong that can be directly sampled.

## Slide 39: Key Idea
Project 4D BRDF into sum of products of 2D function dependent on and 2D function dependent on :
depends only on the incoming direction and
some re-parameterization of the hemisphere.
Notes: Needs animation to promote description of this key contribution…

## Slide 40: 300 Samples/Pixel
Sampling Lafortune Fit
Our Method