## Slide 1: Computer Graphics II: Rendering
CSE 168 [Spr 24], Lecture 3: Illumination and Reflection Ravi Ramamoorthi
http://viscomp.ucsd.edu/classes/cse168/sp24

## Slide 2: To Do
Homework 1 (ray tracer) due Monday
Next assignment direct lighting (on UCSD online). Will cover that material next week

## Slide 3: Illumination Models
Local Illumination
  Light directly from light sources to surface
  No shadows (cast shadows are a global effect)
Global Illumination: multiple bounces (indirect light)
  Hard and soft shadows
  Reflections/refractions (already seen in ray tracing)
  Diffuse and glossy interreflections (radiosity, caustics)
Some images courtesy Henrik Wann Jensen

## Slide 4: Diffuse Interreflection
Diffuse interreflection, color bleeding [Cornell Box]

## Slide 5: Radiosity

## Slide 6: Caustics
Caustics: Focusing through specular surface
Major research effort in 80s, 90s till today

## Slide 7: Motivation: BRDFs, Radiometry
Basics of Illumination, Reflection
Formal radiometric analysis (not ad-hoc)
Reflection Equation (Local Illumination)
Discussion of BRDFs
Rendering Equation (Global Illumination) on Thu
Formal analysis important for correct implementation

## Slide 9: Radiometry
Physical measurement of electromagnetic energy
Measure spatial (and angular) properties of light
  Radiance, Irradiance
  Reflection functions: Bi-Directional Reflectance Distribution Function or BRDF
  Reflection Equation
  Simple BRDF models

## Slide 14: Radiance
Power per unit projected area perpendicular to the ray per unit solid angle in the direction of the ray
Symbol: L(x,ω) (W/m2 sr)
Flux given by dΦ = L(x,ω) cos θ dω dA

## Slide 15: Radiance properties
Radiance constant as propagates along ray
  Derived from conservation of flux
  Fundamental in Light Transport.

## Slide 18: Radiance properties
Sensor response proportional to radiance (constant of proportionality is throughput)
  Far away surface: See more, but subtends smaller angle
  Wall equally bright across viewing distances
Consequences
  Radiance associated with rays in a ray tracer
  Other radiometric quants derived from radiance
  This course primarily about computing radiance

## Slide 19: Irradiance, Radiosity
Irradiance E is radiant power per unit area
Integrate incoming radiance over hemisphere
  Projected solid angle (cos θ dω)
  Uniform illumination: Irradiance = π [CW 24,25]
  Units: W/m2
Radiant Exitance (radiosity)
  Power per unit area leaving surface (like irradiance)

## Slide 23: Irradiance Environment Maps
Incident Radiance
(Illumination Environment Map)
Irradiance Environment Map
R
N

## Slide 24: Radiometry
Physical measurement of electromagnetic energy
Measure spatial (and angular) properties of light
  Radiance, Irradiance
  Reflection functions: Bi-Directional Reflectance Distribution Function or BRDF
  Reflection Equation
  Simple BRDF models

## Slide 28: Building up the BRDF
Bi-Directional Reflectance Distribution Function [Nicodemus 77]
Function based on incident, view direction
Relates incoming light energy to outgoing
Unifying framework for many materials

## Slide 30: BRDF
Reflected Radiance proportional Irradiance
Constant proportionality: BRDF
Ratio of outgoing light (radiance) to incoming light (irradiance)
  Bidirectional Reflection Distribution Function
  (4 Vars) units 1/sr

## Slide 33: Isotropic vs Anisotropic
Isotropic: Most materials (you can rotate about normal without changing reflections)
Anisotropic: brushed metal etc. preferred tangential direction
Isotropic
Anisotropic

## Slide 35: Reflection Equation
Reflected Light
(Output Image)
Emission
Incident
Light (from
light source)
BRDF
Cosine of
Incident angle

## Slide 36: Reflection Equation
Reflected Light
(Output Image)
Emission
Incident
Light (from
light source)
BRDF
Cosine of
Incident angle
Sum over all light sources

## Slide 37: Reflection Equation
Reflected Light
(Output Image)
Emission
Incident
Light (from
light source)
BRDF
Cosine of
Incident angle
Replace sum with integral

## Slide 38: Environment Maps
Light as a function of direction, from entire environment
Captured by photographing a chrome steel or mirror sphere
Accurate only for one point, but distant lighting same at other scene locations (typically use only one env. map)
Blinn and Newell 1976, Miller and Hoffman, 1984
Later, Greene 86, Cabral et al. 87

## Slide 39: Environment Maps
Environment maps widely used as lighting representation
Many modern methods deal with offline and real-time rendering with environment maps
Image-based complex lighting + complex BRDFs

## Slide 40: Radiometry
Physical measurement of electromagnetic energy
Measure spatial (and angular) properties of light
  Radiance, Irradiance
  Reflection functions: Bi-Directional Reflectance Distribution Function or BRDF
  Reflection Equation
  Simple BRDF models

## Slide 41: Brdf Viewer plots
Diffuse
bv written by Szymon Rusinkiewicz
Torrance-Sparrow
Anisotropic

## Slide 44: Specular Term (Phong)

## Slide 47: Torrance-Sparrow
Fresnel term:
allows for wavelength dependency
Geometric Attenuation:
reduces the output based on the amount of shadowing or masking that occurs.
Distribution:
distribution function determines what percentage of microfacets are oriented to reflect in the viewer direction.
How much of the macroscopic surface is visible to the light source
How much of the macroscopic surface is visible to the viewer

## Slide 48: Other BRDF models
Empirical: Measure and build a 4D table
Anisotropic models for hair, brushed steel
Cartoon shaders, funky BRDFs
Capturing spatial variation
Very active area of research