## Slide 1: Real-Time High Quality Rendering
CSE 274 [Fall 2015], Lecture 5
Tour of Modern Offline Rendering
http://www.cs.ucsd.edu/~ravir

## Slide 2: To Do
Project milestone (1-2 pages), final project proposal
  Due on Oct 27
Please get in touch with me if want to meet, have problems

## Slide 3: Motivation for Lecture
Must understand modern offline rendering, before considering real-time extensions
Papers discuss ways to accelerate some effects
Many more interesting possibilities ahead

## Slide 4: Monte Carlo Path Tracing
General solution to rendering and global illumination
Suitable for a variety of general scenes
Based on Monte Carlo methods
Enumerate all paths of light transport
Long history, traces back to rendering eqn Kajiya 86
Increasingly, basis for production rendering
Path tracing today real-time in hardware (for example, using NVIDIA’s Optix)

## Slide 5: Monte Carlo Path Tracing
Big diffuse light source, 20 minutes
Jensen

## Slide 6: Monte Carlo Path Tracing
1000 paths/pixel
Jensen

## Slide 7: Monte Carlo Path Tracing
Advantages
  Any type of geometry (procedural, curved, ...)
  Any type of BRDF (specular, glossy, diffuse, ...)
  Samples all types of paths (L(SD)*E)
  Accuracy controlled at pixel level
  Low memory consumption
  Unbiased - error appears as noise in final image
Disadvantages (standard Monte Carlo problems)
  Slow convergence (square root of number of samples)
  Noise in final image

## Slide 8: Monte Carlo Path Tracing
Integrate radiance for each pixel by sampling paths randomly
Diffuse Surface
Eye
Light
x
Specular Surface
Pixel

## Slide 9: Simplest Monte Carlo Path Tracer
For each pixel, cast n samples and average
  Choose a ray with p=camera, d=(θ,ϕ ) within pixel
  Pixel color += (1/n) * TracePath(p, d)
TracePath(p, d) returns (r,g,b) [and calls itself recursively]:
  Trace ray (p, d) to find nearest intersection p’
  Select with probability (say) 50%:
    Emitted: return 2 * (Lered, Legreen, Leblue) // 2 = 1/(50%)
    Reflected: generate ray in random direction d’ return 2 * fr(d d’) * (nd’) * TracePath(p’, d’)

## Slide 10: Simplest Monte Carlo Path Tracer
For each pixel, cast n samples and average over paths
  Choose a ray with p=camera, d=(θ,ϕ) within pixel
  Pixel color += (1/n) * TracePath(p, d)
TracePath(p, d) returns (r,g,b) [and calls itself recursively]:
  Trace ray (p, d) to find nearest intersection p’
  Select with probability (say) 50%:
    Emitted: return 2 * (Lered, Legreen, Leblue) // 2 = 1/(50%)
    Reflected: generate ray in random direction d’ return 2 * fr(d d’) * (nd’) * TracePath(p’, d’)

## Slide 11: Simplest Monte Carlo Path Tracer
For each pixel, cast n samples and average
  Choose a ray with p=camera, d=(θ,ϕ ) within pixel
  Pixel color += (1/n) * TracePath(p, d)
TracePath(p, d) returns (r,g,b) [and calls itself recursively]:
  Trace ray (p, d) to find nearest intersection p’
  Select with probability (say) 50%:
    Emitted: return 2 * (Lered, Legreen, Leblue) // 2 = 1/(50%)
    Reflected: generate ray in random direction d’ return 2 * fr(d d’) * (nd’) * TracePath(p’, d’)
Weight = 1/probability
Remember: unbiased
requires having f(x) / p(x)

## Slide 12: Simplest Monte Carlo Path Tracer
For each pixel, cast n samples and average
  Choose a ray with p=camera, d=(θ,ϕ) within pixel
  Pixel color += (1/n) * TracePath(p, d)
TracePath(p, d) returns (r,g,b) [and calls itself recursively]:
  Trace ray (p, d) to find nearest intersection p’
  Select with probability (say) 50%:
    Emitted: return 2 * (Lered, Legreen, Leblue) // 2 = 1/(50%)
    Reflected: generate ray in random direction d’ return 2 * fr(d d’) * (nd’) * TracePath(p’, d’)
Path terminated when
Emission evaluated

## Slide 14: Arnold Renderer (M. Fajardo)
Works well diffuse surfaces, hemispherical light

## Slide 15: From UCB CS 294 a few years ago
Daniel Ritchie and Lita Cho

## Slide 16: Importance Sampling
Pick paths based on energy or expected contribution
  More samples for high-energy paths
  Don’t pick low-energy paths
At “macro” level, use to select between reflected vs emitted, or in casting more rays toward light sources
At “micro” level, importance sample the BRDF to pick ray directions
Tons of papers in 90s on tricks to reduce variance in Monte Carlo rendering
Importance sampling now standard in production. I consulted on Pixar’s system for upcoming movies

## Slide 17: Importance Sampling
Can pick paths however we want, but contribution weighted by 1/probability
  Already seen this division of 1/prob in weights to emission, reflectance
x1
xN
E(f(x))

## Slide 18: Importance sample Emit vs Reflect
TracePath(p, d) returns (r,g,b) [and calls itself recursively]:
  Trace ray (p, d) to find nearest intersection p’
  If Le = (0,0,0) then pemit= 0 else pemit= 0.9 (say)
  If random() < pemit then:
    Emitted: return (1/ pemit) * (Lered, Legreen, Leblue)
    Else Reflected: generate ray in random direction d’ return (1/(1- pemit)) * fr(d d’) * (nd’) * TracePath(p’, d’)

## Slide 19: More variance reduction
Discussed “macro” importance sampling
  Emitted vs reflected
How about “micro” importance sampling
  Shoot rays towards light sources in scene
  Distribute rays according to BRDF

## Slide 21: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching

## Slide 22: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching
RenderPark

## Slide 23: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching
Heinrich

## Slide 24: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching
Unfiltered
Filtered
Jensen

## Slide 25: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching
Adaptive
Fixed
Ohbuchi

## Slide 26: Monte Carlo Extensions
Unbiased
  Bidirectional path tracing
  Metropolis light transport
Biased, but consistent
  Noise filtering
  Adaptive sampling
  Irradiance caching
Jensen

## Slide 27: Summary
Monte Carlo methods robust and simple (at least until nitty gritty details) for global illumination
Must handle many variance reduction methods in practice
Importance sampling, Bidirectional path tracing, Russian roulette etc.
Rich field with many papers, systems researched over last 10 years
Today, hardware for real-time ray, path tracing
Promising physically-based GPU approach

## Slide 28: Smoothness of Indirect Lighting
Direct
Indirect
Direct + Indirect

## Slide 29: Irradiance Caching
Empirically, (diffuse) interreflections low frequency
Therefore, should be able to sample sparsely
Irradiance caching samples irradiance at few points on surfaces, and then interpolates
Ward, Rubinstein, Clear. SIGGRAPH 88, A ray tracing solution for diffuse interreflection

## Slide 30: Irradiance Caching Example
Final Image
Sample Locations

## Slide 31
D. Mitchell 95, Consequences of stratified sampling in graphics

## Slide 32: Comparison of simple patterns
Ground Truth
Uniform
Random
Stratified
Latin Hypercube
Quasi Monte Carlo
16 samples for area light, 4 samples per pixel, total 64 samples
Figures courtesy Tianyu Liu
If interested, see my recent paper “A Theory of Monte Carlo Visibility Sampling”

## Slide 33: Path Tracing: From Lights
Step 1. Choose a light ray
Step 2. Find ray-surface intersection
Step 3. Reflect or transmit
  u = Uniform()
  if u < reflectance(x)
  Choose new direction d ~ BRDF(O|I)
  goto Step 2
else if u < reflectance(x)+transmittance(x)
  Choose new direction d ~ BTDF(O|I)
  goto Step 2
else // absorption=1–reflectance-transmittance
  terminate on surface; deposit energy

## Slide 34: Bidirectional Path Tracing
Path pyramid (k = l + e = total number of bounces)

## Slide 35: Comparison

## Slide 36: Why Photon Map?
Some visual effects like caustics hard with standard path tracing from eye
May usually miss light source altogether
Instead, store “photons” from light in kd-tree
Look-up into this as needed
Combines tracing from light source, and eye
Similar to bidirectional path tracing, but compute photon map only once for all eye rays
Global Illumination using Photon Maps H. Jensen. Rendering Techniques (EGSR 1996), pp 21-30. (Also book: Realistic Image Synthesis using Photon Mapping)

## Slide 37: Caustics
Slides courtesy Henrik Wann Jensen
Path Tracing: 1000 paths/pixel
Note noise in caustics

## Slide 38: Caustics
Photon Mapping: 10000 photons
50 photons in radiance estimate

## Slide 39: Reflections Inside a Metal Ring
50000 photons
50 photons to estimate radiance

## Slide 40: Caustics on Glossy Surfaces
340000 photons, 100 photons in radiance estimate

## Slide 41: HDR Environment Illumination

## Slide 42: Global Illumination

## Slide 43: Direct Illumination

## Slide 44: Specular Reflection

## Slide 45: Caustics

## Slide 46: Indirect Illumination

## Slide 47: Mies House: Swimming Pool

## Slide 48: Lightcuts
Efficient, accurate complex illumination
Environment map lighting & indirect
Time 111s
Textured area lights & indirect
Time 98s
(640x480, Anti-aliased, Glossy materials)
From Walter et al. SIGGRAPH 05
Notes: What is lightcuts? Lightcuts is a new scalable solution for efficiently computing complex illumination. Two examples are shown here. The image on the left is lit by an environment map with illumination captured from the real world, while the image on the right includes two simulated high dynamic range flat-panel displays. Both are challenging illumination problems. In addition both images include indirect illumination, glossy materials, and anti-aliasing. Yet our method was able to produce each image in under two minutes on a single machine.

## Slide 49: Complex Lighting
Simulate complex illumination using point lights
  Area lights
  HDR environment maps
  Sun & sky light
  Indirect illumination
Unifies illumination
  Enables tradeoffs between components
Area lights + Sun/sky + Indirect
Notes: Once we have a scalable solution for many point lights, we can use this to compute other types of complex illumination. The four examples we demonstrate in the paper are area lights, high dynamic range environment maps, sun & sky light, and indirect illumination. Moreover this allows us to unify the handling of different illumination types and enables new types of tradeoffs. For example, bright illumination from one source allows coarser approximations of other sources.

## Slide 50: Key Concepts
Light Cluster
Light Tree
  Binary tree of lights and clusters
Clusters
Individual
Lights
Notes: Second is the light tree which is a binary tree of lights and clusters. The leaves of this tree are the individual lights while the interior nodes represent clusters which get progressively larger as we go up the tree.

## Slide 51: Three Example Cuts
1
2
3
4
1
4
4
1
2
3
4
1
4
4
1
2
3
4
1
4
4
Three Cuts
#1
#2
#4
#1
#3
#4
#1
#4
Notes: And here we show three example cuts through the light tree. Highlighted above each cut are the regions where that cut produces an accurate approximation of the exact illumination.

## Slide 52
Tableau, 630K polygons, 13 000 lights, (EnvMap+Indirect)
Avg. shadow rays per eye ray 17 (0.13%)
Notes: Here is another results that show cases our ability to handle glossy objects. This scene is illuminated by a captured environment map and indirect illumination. And here is a short animation of this scene.

## Slide 53: Adaptive Wavelet Rendering